TULSA GAS TECHNOLOGIES, INC.

4809 South 101 East Avenue

TULSA OK 74146

PHONE: 918-665-2641               FAX: 918-665-2641

Chart of values for the LMS Control Board.

#### VOLTAGE

The Voltage across the photosensor with the sensor installed with the light in the position that you want the reaction.  5VDC Max. Values are approximate but are very close.

LMS SETTING

The position of the knob for the individual light set point.

RESISTANCE VALUE

Resistance of the photocell not connected in the system with the light in the position that you

want the reaction. Values are approximate but are very close.

#### VOLTAGE	LMS SETTING                    	RESISTANCE VALUE

5.00 – 4.89	ON

4.88	1	38K – 34.9K ohms

4.82 – 4.79	2	20.8K – 18.6K ohms

4.22 – 4.26	3	10.1K ohms

3.66 – 3.70	4	6K ohms

2.98	5	4.7K ohms

2.40	6	3.1K ohms

1.8	7	1.9K ohms

1.22	8	.88K ohms

.69	9	.59K ohms

.63	10	.38K ohms