Tulsa Gas Technologies, Inc.

4809 S. 101st East Ave     Tulsa, OK 74146

#### PHONE: 918-665-2641    FAX: 918-665-2657

###### 1/4/2017

Dispenser Serial Number 16121145

SIDE 1

Micro Motion Transmitter Configuration

Required settings for correct operation of Micro Motion mass flow meter.

Transmitter Model Number:	2700

Sensor Model Number:	CNG050

Transmitter Serial Number:    3353444

Sensor Serial Number		13126040

Flow Calibration Factor:	139.784.50

Flow Units			L/min

Communication on RS-485

Protocol			Modbus ASCII 7 Bit

Modbus Address		1

Baud Rate			1200

Parity				Odd

Stop Bits			1

HART Communication

Superimposed on Primary mA (PV)

Analog Output (4-20 mA)

Analog Variable (PV)		Mass Flow

Lower Range Value		00000 lb/min

Upper Range Value		300.000 lb/min

mA Cutoff			0.0000 lb/min

Freq/Rate

Frequency variable (TV)	Mass Flow

Frequency Cutoff		0.2500 lb/min

Pulses per Unit		1000.00000 per lb

Temperature

Temp Units			deg C